## Slide 1: Rendering Fractals using the PYNQ Framework on FPGAs
PYNQ: Python Productivity for Zynq
Zynq System on Chip integrates an ARM processor with FPGA logic
Hardware “overlay” design is used to program the FPGA part of Zynq
Python API interacts with overlay
4th year CES | Student: | Filip Lejhanec
EE475 Project | 1st Supervisor: | Dr Louise Helen Crockett
2018/2019 | 2nd Supervisor: | Dr Alexandra Coddington

## Slide 2: Overview of the Problem
Fractal is a recursive, self-similar mathematical set
Initial focus is on the Mandelbrot set:
  Set of complex numbers for which the function does not diverge when iterated from
Colour is derived based on how fast the function diverges
Only a limited number of iterations is calculated
High limits are required to preserve detail at high zoom
Computationally intensive, but (mostly) data parallel

## Slide 3: System Architecture
PyQt GUI
GPU Renderer
SSH Shell
PYNQ-Z1
FPGA Circuit
PC Monitor
HDMI Monitor

## Slide 4: FPGA Architecture
Store Pixel Data
AXI Stream S2MM
Configuration
    Colours
    Coordinates
    Scale
AXI Interconnect
Zynq Processing System
Mandelbrot HW block
AXI Video Direct Memory Access
AXI Stream MM2S
Read Pixel Data
AXI Interrupt Controller
Notify when Finished Processing

## Slide 5: Implementation details
32-bit variables
Fixed point at 4:28
16 parallel processors
FHD output to HDMI
1 frame/second
Customisable
Python API
Floating point
Fixed point
vs.

## Slide 6: Render Times of Different IP Implementations
Chart: Render time (seconds)
| Software implementation | Single pixel calculation | Full image calculation | Optimised IP design
Frames per second (1/s) | 2004.5 | 1025.3 | 227.6 | 0.92